## Slide 1
Liver Tumor Segmentation
Using Deep Learning
A Comprehensive Survey and Comparative Analysis
[Student Name] | [Guide Name]
Dept. of Computer Science & Engineering | MIT World Peace University, Pune
IEEE Conference Paper • 2024–25

## Slide 2
2 / 14
Presentation Outline
01
Introduction & Motivation
Why liver tumor segmentation matters
02
Background & Related Work
Clinical context and classical methods
03
Methodology Overview
Preprocessing, metrics, loss functions
04
U-Net Family & Encoder–Decoders
ResUNet, AIM-Unet, EREs-UNet++, nnU-Net
05
Attention & Transformer Models
UNETR, Swin-UNet, FUF-TransUNet, G-UNETR++
06
GAN & Semi-Supervised Methods
MedGAN, FedLiverNet, SAM + GAN
07
Results & Comparison
LiTS benchmark, cross-dataset generalization
08
Challenges & Future Directions
Open problems and research frontiers

## Slide 3
3 / 14
Introduction & Motivation
3rd
Liver Cancer
Mortality Rank
865K
New Cases
per Year
<20%
5-Year
Survival Rate
60 min
Manual Seg.
per CT Volume
Key Segmentation Challenges
Class Imbalance:
Tumor voxels < 3% of total CT volume; often < 0.5% for early lesions
Morphological Variability:
Tumors range from 4 mm nodules to 187 mm masses in LiTS
Low Contrast:
Hypovascular tumors near-isodense to liver parenchyma in early CT phase
Annotation Scarcity:
LiTS has only 131 labelled volumes; annotation takes 20–60 min/case
Domain Shift:
5–10% Dice drop when transferring across institutions or scanner protocols

## Slide 4
4 / 14
Background & Related Work
CT Imaging for Liver
Liver parenchyma: 50–70 HU
Hypovascular tumors: 20–40 HU
Hypervascular HCC: 80–120 HU (arterial phase)
HU windowing: [−200, 250] for soft tissue
Z-score normalization per volume
Isotropic resampling: 1.0 × 1.0 × 1.0 mm³
Classical ML Methods (Pre-DL)
• SVM + GLCM features → ~82% accuracy
• Random Forest + HOG/LBP descriptors
• Parameter-sensitive; no hierarchical features
• Cannot capture complex tumor morphology
LiTS Benchmark Dataset
• 201 abdominal CT volumes (131 train / 70 test)
• 7 hospitals • 3 scanner manufacturers
• 1,224 tumor instances in training set
• Tumor diameter: 4 mm – 187 mm (median 32 mm)
• Tumor Dice: 0.52 (2017) → 0.78 (2022)

## Slide 5
5 / 14
Methodology: Preprocessing, Metrics & Loss Functions
HU
Windowing
Spatial
Resampling
Z-Score
Norm.
Data
Augmentation
Network
Training
Post-
Processing
Evaluation Metrics
Dice Coeff.
2|X∩Y| / (|X|+|Y|)
Primary overlap metric
IoU / Jaccard
|X∩Y| / |X∪Y|
Area of overlap / union
ASD (mm)
Mean surface distance
Boundary accuracy
Hausdorff (mm)
Max surface distance
Worst-case boundary
Sensitivity
TP / (TP + FN)
Tumor voxel recall
Loss Functions
Dice Loss
Directly optimizes overlap; class-imbalance robust
Focal Loss
Down-weights easy negatives; γ=2 for hard examples
Tversky Loss
β>0.5 → prioritises recall for small tumors
Compound (Dice+Focal)
Most effective in practice for imbalanced datasets

## Slide 6
03
Deep Learning Architectures
U-Net Family • Attention Models • Vision Transformers • GANs • Semi-supervised
ARCHITECTURAL PARADIGMS FOR LIVER TUMOR SEGMENTATION

## Slide 7
7 / 14
U-Net Family & Encoder–Decoder Variants
Architecture | Key Innovation | Tumor Dice (LiTS)
U-Net (2015) | Encoder-decoder + skip connections; biomedical baseline | –
V-Net (2016) | 3D volumetric U-Net; introduced Dice loss as objective | ~0.750
H-DenseUNet (2018) | Hybrid 2D+3D dense connections; state-of-art at launch | 0.780
UNet++ (2018) | Nested dense skip connections; closes encoder-decoder gap | 0.765
ResUNet (2022) | Residual blocks in encoder; mitigates vanishing gradients | 0.792
nnU-Net (2021) | Self-configuring; auto preprocessing + topology selection | 0.810
AIM-Unet (2023) | Inception modules: 1×1, 3×3, 5×5 parallel convolutions | ~0.800
EREs-UNet++ (2023) | High-Efficiency Channel Attention in nested UNet++ | 0.779

## Slide 8
8 / 14
Attention & Vision Transformer Architectures
Attention-Augmented U-Nets
Attention U-Net (2018)
Additive attention gates at skip connections; α = σ(Wα·ReLU(Wg·g + Wx·x))
RA-UNet (2020)
Residual + attention gates; Liver 0.960 / Tumor 0.741
RMAU-Net (2023)
Multi-scale dilated conv {1,2,4} + attention; Tumor 0.762
CPAD-Net (2023)
Dual SE+spatial attention on dilated branches {1,2,4,8}
MDAUnet (2024)
Deformable attention; multi-task seg + classification; 0.783
Vision Transformer Models
UNETR (2022)
Pure ViT encoder (12 layers); CNN decoder; 16³ patches; Tumor 0.772
Swin-UNet (2022)
Shifted-window attention O(N); patch merge/expand; Tumor 0.762
nnFormer (2023)
Interleaved local+global 3D attention; Tumor 0.778 on LiTS
TD-Net (2023)
Dual-path Transformer + dilated CNN; Liver 0.962, Tumor 0.763
FUF-TransUNet (2024)
DS + SFF modules on TransUNet; Tumor 0.834 (LiTS) / 0.898 (3DIRCADb)
G-UNETR++ (2026)
Gradient-enhanced UNETR; ASD 5.8 mm; Tumor 0.844 on LiTS

## Slide 9
9 / 14
GAN, Semi-Supervised & Federated Learning Approaches
GAN-Based Augmentation
MedGAN (2023)
Progressive multi-phase CT synthesis; adaptive cGAN; targets under-represented imaging phases
MA-CGAN (2024)
Multi-axis attention + conditional GAN loss; −18% Hausdorff Distance; +6.2% recall for <2 cm lesions
Dual GAN (2023)
Cycle-consistency between non-contrast and contrast CT; unpaired cross-phase augmentation
Semi-Supervised & Self-Supervised
Label-Free Seg. (CVPR 2023)
SAM pseudo-labels → 0.760 Tumor Dice with zero manual annotation
Multi-View SSL (2025)
Foundation model regularizer + axial/sagittal/coronal views; 20 labelled cases → 83.8% liver Dice
Self-Supervised Swin (2022)
Masked CT image modelling pretraining; strong fine-tuning with <30% labels
Federated Learning
FedLiverNet (2025)
Differential privacy aggregation; clustered FL; within 5% of centralised training
FL-SANet (2025)
Teacher-student SANet; semi-supervised pseudo-labels; privacy-preserving multi-site
SAM + GAN (2023)
Foundation model + GAN domain adaptation; Tumor Dice 0.943 (best on LiTS)

## Slide 10
10 / 14
Quantitative Results: LiTS Benchmark Comparison
Method | Year | Liver DC ↑ | Tumor DC ↑ | ASD ↓ (mm) | Type
Cascade FCN | 2017 | 0.946 | 0.675 | — | CNN
H-DenseUNet | 2018 | 0.961 | 0.780 | — | CNN
RA-UNet | 2020 | 0.960 | 0.741 | 14.8 | Attention
U-n-Net | 2020 | 0.951 | 0.741 | 21.3 | CNN
ResUNet | 2022 | 0.958 | 0.792 | 8.7 | U-Net
nnU-Net | 2021 | 0.963 | 0.810 | 7.9 | Self-config
UNETR | 2022 | 0.952 | 0.772 | 11.2 | Transformer
AIM-Unet | 2023 | 0.964 | 0.800 | 8.6 | U-Net
TD-Net | 2023 | 0.962 | 0.763 | 8.4 | Hybrid
MDAUnet | 2024 | 0.965 | 0.783 | 8.0 | Attention
FUF-TransUNet | 2024 | 0.968 | 0.834 | 6.9 | Transformer
G-UNETR++ | 2026 | 0.971 | 0.844 | 5.8 | Transformer
SAM + GAN | 2023 | 0.976 | 0.943 | 5.1 | Foundation

## Slide 11
11 / 14
Tumor Dice Score Progression Across Architectures (LiTS)
Chart: 
| Cascade FCN 2017 | H-DenseUNet 2018 | RA-UNet 2020 | ResUNet 2022 | nnU-Net 2021 | UNETR 2022 | AIM-Unet 2023 | FUF-TransUNet 2024 | G-UNETR++ 2026 | SAM+GAN 2023
Tumor Dice | 0.675 | 0.78 | 0.741 | 0.792 | 0.81 | 0.772 | 0.8 | 0.834 | 0.844 | 0.943

## Slide 12
12 / 14
Cross-Dataset Generalization & Key Observations
Cross-Dataset: LiTS → 3DIRCADb
Method | LiTS DC | 3DIRCADb DC | Drop
RA-UNet | 0.741 | 0.680 | −8.2%
ResUNet | 0.792 | 0.734 | −7.3%
AIM-Unet | 0.800 | 0.754 | −5.8%
nnU-Net | 0.810 | 0.771 | −4.8%
G-UNETR++ | 0.844 | 0.832 | −1.4%
G-UNETR++ shows best cross-scanner robustness (−1.4% only)
thanks to gradient-enhanced scanner-agnostic features.
Key Observations
Liver Dice Saturated
All methods achieve 0.94–0.98; tumor segmentation remains dominant challenge
Transformer Advantage
Global self-attention improves boundary-adjacent & small tumor accuracy
Two-Stage Pipeline
Liver ROI → tumor seg outperforms single-stage by 5–10% Dice
Compound Loss
Dice + Focal consistently outperforms single-loss for class imbalance
nnU-Net Baseline
Self-configuration (0.810) beats many manually designed post-2021 architectures
ASD Halved
Boundary ASD dropped from 14–21 mm (2020) to 5.1–6.9 mm (2024)

## Slide 13
13 / 14
Open Challenges & Future Research Directions
Open Challenges
Small Tumor Detection
Sensitivity <0.50 for sub-cm lesions; critical for early HCC surveillance at 1 cm threshold
Class Imbalance
Tumor voxels <3% of volume; even <0.1% for early lesions; compound losses insufficient
Domain Shift
5–8% Dice drop across institutions; instance norm and TTA provide partial mitigation
Annotation Cost
131 LiTS volumes vs. billion-scale natural image datasets; SSL/WSL essential
Clinical Validation
No prospective workflow integration or regulatory evidence in any reviewed study
Compute Cost
3D transformers require 40–120 GB VRAM; 2–10 min inference/volume
Future Research Directions
Foundation Model Fine-Tuning
LoRA adapter tuning on SAM/MedSAM with <50 annotated CT cases
Federated Multi-site Training
GDPR/HIPAA-compliant FL with differential privacy and personalized local heads
Self-Supervised Pretraining
Masked CT image modelling on hospital PACS archives (millions of unlabelled scans)
Uncertainty Quantification
MC Dropout / deep ensembles → per-voxel confidence for human-AI collaboration
Multi-Phase & Multi-Modal Fusion
Arterial + portal-venous + delayed CT; CT + MRI with cross-modal attention
Lightweight Real-Time Inference
MobileNetV2 encoder + INT8 quantization → <100 ms for intraoperative use

## Slide 14
Conclusion
Architectural Progress
Tumor Dice: 0.675 (2017 CNN) → 0.834–0.844 (2024 Transformers) → 0.943 (SAM+GAN foundation model)
Liver Seg. Solved
Liver Dice >0.96 achieved consistently; tumor segmentation is the dominant remaining challenge
Two-Stage Pipelines Win
Liver ROI localization → tumor segmentation consistently outperforms end-to-end single-stage methods
Domain Shift Persists
5–8% Dice performance drop across institutions remains the primary clinical translation barrier
Data Efficiency Critical
Semi-supervised (20 labels → 60% tumor Dice) and federated learning are essential for deployment
Future: Foundation Models
SAM-Med3D, self-supervised CT pretraining, and lightweight deployment are highest-priority directions
MIT World Peace University • Dept. of Computer Science & Engineering • [Student Name] | [Guide Name]
Thank You • Questions Welcome